## Slide 1
Home Monitoring System
Final Presentation

## Slide 2
INTRODUCTION
DEMONSTRATION
PROBLEM AND OVERCOME
FUTURE IMPLEMENTATION
ADVICES FOR FUTURE

## Slide 3
Welcome to the presentation of our home monitoring system project, a versatile robotics project designed to enhance home security and automation using an Arduino Uno microcontroller. The system integrates multiple sensors and actuators to provide real-time monitoring and response to various environmental and security conditions within a home.
1
INTRODUCTION

## Slide 4
The servo motor operates the door, allowing automated opening and closing based on sensor inputs.
Servo Motor for Door Control
The Passive Infrared (PIR) sensor detects the presence of a person. Upon detection, it triggers an alarm system to alert the occupants.
PIR Sensor for Person Detection and Alarm System
2
Demonstration of working Robot
An Infrared (IR) sensor is used to sense the presence of a person at the door. When someone approaches, the door automatically opens.
IR Sensor for Door Activation
The MQ-7 sensor detects carbon monoxide levels in the environment. If dangerous levels are detected, an alarm is triggered to alert the occupants.
MQ-7 Gas Sensor
The LCD display provides real-time data about the system's status, including temperature readings and alerts.
16x2 LCD Display
Buzzer is used to provide distinct alarm sounds for different alerts.
Buzzer for Alarms
A DC motor is used to control a fan. The fan is activated when the temperature exceeds 30°C. If the temperature rises above 40°C, an additional alarm is triggered to indicate the extreme heat condition.
DC Motor for Fan Control

## Slide 5
Sensor Calibration
Integration Challenges
Environmental Interference
Power Management
3
Problems Faced and How We Overcame Them

## Slide 6
01
Problem: Integrating multiple sensors and actuators with the Arduino Uno posed significant challenges, including limited I/O pins and managing simultaneous operations.
Solution: We used an I2C device to connect the LCD display, thereby reducing the number of pins needed.
Integration Challenges

## Slide 7
02
Problem: The PIR and IR sensors required precise calibration to avoid false positives and ensure reliable detection.
Solution: We conducted extensive testing and fine-tuning of sensor thresholds and placement to achieve optimal sensitivity and accuracy.
Sensor Calibration

## Slide 8
03
Problem: Managing power consumption with multiple components running simultaneously was a challenge.
Solution: We optimized the power usage by implementing sleep modes for sensors and actuators when not in use, and used a dedicated power supply to ensure stable operation.
Power Management

## Slide 9
04
Problem: Environmental factors such as lighting and temperature fluctuations affected sensor readings.
Solution: We used shielding and appropriate sensor placement to minimize interference. Additionally, software filters and algorithms were implemented to smooth out sensor data.
Environmental Interference

## Slide 10
Start with a Clear Plan: Define the scope and objectives of your project clearly before beginning the development process.
Modular Design: Design your system in a modular way so that components can be tested and replaced independently.
Thorough Testing: Conduct thorough testing under different conditions to ensure reliability and robustness.
Documentation: Keep detailed documentation of your design, code, and troubleshooting steps to facilitate future modifications and improvements.
Community Resources: Utilize online communities and resources for troubleshooting and gaining insights into best practices.
4
Advices for future researchers

## Slide 11
Remote Monitoring and Control: Integrate IoT capabilities to allow remote monitoring and control of the home monitoring system through a smartphone app.
Advanced Analytics: Implement data analytics to provide insights and trends based on sensor data, enhancing predictive maintenance and security.
Voice Control: Add voice control capabilities using platforms like Amazon Alexa or Google Assistant for hands-free operation.
Enhanced Security Features: Integrate facial recognition or fingerprint sensors for enhanced security at the door.
Energy Management: Implement smart energy management systems to optimize power consumption based on real-time data and usage patterns.
5
Future Implementations

## Slide 12
THANK YOU
for your attention and interest in our Home Monitoring System project. Your feedback and questions are greatly appreciated!